## Slide 1
AVESTA · EGYPT RESIDENTIAL
Home Tier Sizing
The equations behind the tool, from the customer's bill to battery size, savings and payback
Worked example on every slide: a monthly bill of 2,000 EGP

## Slide 2
OVERVIEW
Five steps from a bill to a recommendation
1
Input
Last bill (EGP) or last month (kWh)
2
Consumption
Bill → kWh, split into day and night
3
Sizing
Solar PV (kWp) and battery (kWh)
4
New bill
Grid import after solar, billed by tier
5
Economics
Price, savings, payback, backup
Example: 2,000 EGP → 851 kWh per month → Solar only 3 kWp, or Solar + battery 6.5 kWp with 21.12 kWh

## Slide 3
INPUT DATA
Residential tariff tiers (August 2026 bill)
Tier | Monthly kWh | EGP / kWh | How it bills
1 | 0 – 50 | 0.68 | Progressive
2 | 51 – 100 | 0.87 | Progressive
3 | 101 – 200 | 1.00 | Progressive; above 100 kWh the first 200 all bill at 1.00
4 | 201 – 350 | 1.73 | Progressive
5 | 351 – 650 | 2.18 | Progressive
6 | 651 – 1000 | 2.35 | Flat on ALL kWh
7 | > 1000 | 2.89 | Flat on ALL kWh
Fees and future tariff increases are ignored. Rates are editable in the tool.
Sources: Youm7 and Masrawy, 1 August 2026

## Slide 4
STEP 2 · TARIFF
Monthly bill from consumption M (kWh)
Consumption | Bill (EGP)
M ≤ 50 | 0.68 × M
50 < M ≤ 100 | 34 + 0.87 × (M − 50)
100 < M ≤ 650 | 1.00 × min(M, 200) + 1.73 × max(0, min(M, 350) − 200) + 2.18 × max(0, M − 350)
650 < M ≤ 1000 | 2.35 × M
M > 1000 | 2.89 × M
Check values
M (kWh) | Bill (EGP)
90 | 68.8
300 | 373.0
500 | 786.5
800 | 1,880.0
1,200 | 3,468.0

## Slide 5
STEP 2 · BILL → KWH
First, the bill at each tier boundary
Consumption | Calculation | Bill (EGP)
50 kWh | 50 × 0.68 | 34
100 kWh | 34 + 50 × 0.87 | 77.5
200 kWh | 200 × 1.00 | 200
350 kWh | 200 + 150 × 1.73 | 459.5
650 kWh | 459.5 + 300 × 2.18 | 1,113.5
1000 kWh | 1000 × 2.35 | 2,350
Method
1. Find the tier: compare the bill with these boundary bills.
2. Subtract the cost of the tiers below it.
3. Divide what is left by that tier's rate.
Above 100 kWh the first 200 kWh all bill at 1.00; above 650 kWh all consumption bills at one flat rate.

## Slide 6
STEP 2 · BILL → KWH
Consumption M from the bill B
If the bill B is | Tier | Consumption M (kWh)
up to 34 | 1 | B ÷ 0.68
34 – 77.5 | 2 | 50 + (B − 34) ÷ 0.87
101 – 200 | 3 | B ÷ 1.00
200 – 459.5 | 4 | 200 + (B − 200) ÷ 1.73
459.5 – 1,113.5 | 5 | 350 + (B − 459.5) ÷ 2.18
1,527.5 – 2,350 | 6 | B ÷ 2.35
2,890 and above | 7 | B ÷ 2.89
Bills between 77.5–101, 1,113.5–1,527.5 and 2,350–2,890 have no exact consumption (see the jumps slide).

## Slide 7
STEP 2 · BILL → KWH
Four worked examples
300 EGP
Between 200 and 459.5 → Tier 4
200 + (300 − 200) ÷ 1.73 = 257.8 kWh
1,000 EGP
Between 459.5 and 1,113.5 → Tier 5
350 + (1,000 − 459.5) ÷ 2.18 = 597.9 kWh
2,000 EGP
Between 1,527.5 and 2,350 → Tier 6
2,000 ÷ 2.35 = 851.1 kWh
4,000 EGP
Above 2,890 → Tier 7
4,000 ÷ 2.89 = 1,384.1 kWh

## Slide 8
STEP 2 · BILL → KWH
How the tool computes it, and the bill jumps
M = largest m where Bill(m) ≤ B
The tool gets the same result by bisection (60 halvings, rounded to 0.1 kWh), so it stays correct if the tier rates are edited.
1,000 EGP → 597.9 kWh
2,000 EGP → 851.1 kWh
Bills inside a jump
At | Bill jumps (EGP) | Mapped to
100 kWh | 77.5 → 101 | 100 kWh
650 kWh | 1,113.5 → 1,527.5 | 650 kWh
1000 kWh | 2,350 → 2,890 | 1000 kWh
No consumption gives these bills exactly (fees are the usual cause), so the tool uses the threshold. Better: take the kWh printed on the bill.

## Slide 9
STEP 2 · DAILY ENERGY
Daily consumption and its day / night split
E = M ÷ 30
N = E × night share (default 55%)
D = E − N
28.37
E · kWh per day (851.1 ÷ 30)
15.60
N · kWh at night
12.77
D · kWh in daytime

## Slide 10
STEP 3 · SOLAR PV
Solar array size P (kWp)
Daily generation G = P × Y, where Y = 4.8 kWh per kWp per day
Solar only
P = D ÷ Y
12.77 ÷ 4.8 = 2.66 → 3.0 kWp
Without a battery, solar beyond the daytime load is lost.
Solar + battery
P = (D + min(N, U) ÷ η) ÷ Y
(12.77 + 15.60 ÷ 0.95) ÷ 4.8 = 6.08 → 6.5 kWp
Extra solar charges the battery for the night. U = usable battery energy, η = 95%.
Both sizes round up to the next 0.5 kWp.

## Slide 11
STEP 3 · BATTERY
Battery capacity C (kWh)
C required = N ÷ (DoD × η)
15.60 ÷ (0.80 × 0.95) = 20.53 kWh
Pick the smallest AVESTA combination at or above it: any number of LV_32, plus at most one LV_16 and one LV_5. Ties go to fewer units.
→ LV_16 + LV_5 = 21.12 kWh
Usable U = C × DoD = 16.90 kWh
“Full day” mode uses E instead of N, the original deck's method.
Required kWh | Combination
up to 5.12 | 1 × LV_5
up to 16 | 1 × LV_16
up to 21.12 | LV_16 + LV_5
up to 32 | 1 × LV_32
up to 37.12 | LV_32 + LV_5
up to 48 | LV_32 + LV_16
up to 53.12 | LV_32 + LV_16 + LV_5
up to 64 | 2 × LV_32

## Slide 12
STEP 4 · NEW BILL
Grid import after solar (kWh per day)
Equation | Solar only | Solar + battery
Generation G = P × Y | 14.40 | 31.20
Direct use = min(G, D) | 12.77 | 12.77
Surplus = G − direct | 1.63 (lost) | 18.43
From battery = min(surplus × η, U, N) | 0 | 15.60
Import / day = E − direct − battery | 15.60 | 0
Import / month = × 30 | 468 kWh | 0 kWh
New bill = Bill(import) | 717 EGP · Tier 5 | 0 EGP
Exported surplus earns nothing: savings count only solar energy the home uses itself.

## Slide 13
STEP 5 · ECONOMICS
System price (EGP)
Inverter kW = smallest standard size ≥ max(3, P): 3, 5, 6, 8, 10, 12, 15, 20 …
Price = (P × 8,000 + Inverter × 6,000) × 1.10 + C × 13,640
The 10% for installation & BOS applies to PV and inverter only, not to the battery.
Solar only · 3 kWp, 3 kW inverter
(24,000 + 18,000) × 1.10
46,200
Solar + battery · 6.5 kWp, 8 kW inverter
(52,000 + 48,000) × 1.10 + 288,077
398,077

## Slide 14
STEP 5 · ECONOMICS
Savings, payback and backup
Equation | Solar only | Solar + battery
Monthly saving = Bill(M) − Bill(import) | 1,283 | 2,000
Annual saving = monthly × 12 | 15,397 | 24,001
Payback = Price ÷ annual saving | 3.0 years | 16.6 years
Backup hours = U ÷ (E ÷ 24) | none | ≈ 14.3 h
Recommend solar + battery when its payback ≤ 1.15 × solar-only payback
Backup hours use the average load; peaks such as air conditioning shorten them.

## Slide 15
TIER CLIFF
The kWh just above 650 or 1000 are the most valuable to cut
Value per kWh cut = (Bill(M) − Bill(T)) ÷ (M − T), with T = 650 or 1000
4.41
EGP saved per kWh: (2,000 − 1,113.5) ÷ (851 − 650)
2.35
EGP average price today

## Slide 16
INPUTS
Default assumptions and their sources
Assumption | Default | Source
Night share | 55% | Estimate; needs measured load profiles
PV yield | 4.8 kWh/kWp/day | Cairo ≈ 1,750 kWh/kWp per year
Depth of discharge | 80% | AVESTA LV datasheet: 6,000 cycles at 80%
Round-trip efficiency | 95% | Home Storage deck
Battery price | 13,640 EGP/kWh | Deck: €220 × 62 EGP
PV price | 8,000 EGP/kWp | Deck
Inverter price | 6,000 EGP/kW | Estimate
Installation & BOS | 10% of PV + inverter | Deck: 10–15%
Days per month | 30 | Fixed
All defaults except days per month are editable under “Assumptions & prices” in the tool.