## Slide 1
AVESTA · EGYPT RESIDENTIAL
Home Tier Sizing: the equations
1 Input
2 Consumption
3 Sizing
4 New bill
5 Economics
Tier | Monthly kWh | EGP / kWh | How it bills
1 | 0 – 50 | 0.68 | Progressive
2 | 51 – 100 | 0.87 | Progressive
3 | 101 – 200 | 1.00 | Progressive; above 100 kWh the first 200 all bill at 1.00
4 | 201 – 350 | 1.73 | Progressive
5 | 351 – 650 | 2.18 | Progressive
6 | 651 – 1000 | 2.35 | Flat on ALL kWh
7 | > 1000 | 2.89 | Flat on ALL kWh
Tariff of the August 2026 bill (Youm7, Masrawy). Fees and future increases are ignored. Worked example throughout: a 2,000 EGP bill.
Notes: The five steps: 1 Input: last bill (EGP) or last month (kWh). 2 Consumption: bill to kWh, split into day and night. 3 Sizing: solar PV (kWp) and battery (kWh). 4 New bill: grid import after solar, billed by tier. 5 Economics: price, savings, payback, backup.
Tier rates are editable in the tool. Above 650 kWh, and again above 1000 kWh, the whole consumption bills at one flat rate.

## Slide 2
STEP 2 · BILL ↔ KWH
From consumption to bill, and back
Tier | kWh (M) | Bill from M | Bill at top | M from bill B
1 | 0 – 50 | 0.68 × M | 34 | B ÷ 0.68
2 | 51 – 100 | 34 + 0.87 × (M − 50) | 77.5 | 50 + (B − 34) ÷ 0.87
3 | 101 – 200 | 1.00 × M | 200 | B ÷ 1.00
4 | 201 – 350 | 200 + 1.73 × (M − 200) | 459.5 | 200 + (B − 200) ÷ 1.73
5 | 351 – 650 | 459.5 + 2.18 × (M − 350) | 1,113.5 | 350 + (B − 459.5) ÷ 2.18
6 | 651 – 1000 | 2.35 × M | 2,350 | B ÷ 2.35
7 | > 1000 | 2.89 × M | — | B ÷ 2.89
Bill jumps: 77.5 → 101 (100 kWh) · 1,113.5 → 1,527.5 (650 kWh) · 2,350 → 2,890 (1000 kWh)
Example: 2,000 EGP lies between 1,527.5 and 2,350, so Tier 6: 2,000 ÷ 2.35 = 851.1 kWh. A bill inside a jump maps to the threshold; the kWh printed on the bill is more exact.
Notes: Method: find the tier by comparing the bill with the 'Bill at top' column, subtract the cost of the tiers below, divide the rest by that tier's rate.
Worked examples: 300 EGP -> 200 + (300 - 200) / 1.73 = 257.8 kWh (Tier 4). 1,000 EGP -> 350 + (1,000 - 459.5) / 2.18 = 597.9 kWh (Tier 5). 2,000 EGP -> 2,000 / 2.35 = 851.1 kWh (Tier 6). 4,000 EGP -> 4,000 / 2.89 = 1,384.1 kWh (Tier 7).
Check values of the bill: 90 kWh = 68.8; 300 = 373.0; 500 = 786.5; 800 = 1,880.0; 1,200 = 3,468.0 EGP.
The tool computes the same result by bisection (largest M with Bill(M) <= B, 60 halvings, rounded to 0.1 kWh), so it stays correct if tier rates are edited.

## Slide 3
STEP 3 · SIZING
Daily split, solar size and battery size
Daily energy
E = M ÷ 30
851.1 ÷ 30 = 28.37 kWh
N = E × night share (55%)
15.60 kWh at night
D = E − N
12.77 kWh in daytime
Solar PV (kWp)
P = D ÷ Y
Solar only: 2.66 → 3.0 kWp
P = (D + min(N,U) ÷ η) ÷ Y
Solar + battery: 6.08 → 6.5 kWp
Y = 4.8 kWh/kWp/day, η = 95%. Rounded up to 0.5 kWp.
Battery (kWh)
C = N ÷ (DoD × η)
15.60 ÷ 0.76 = 20.53 kWh
Smallest AVESTA stack ≥ C
LV_16 + LV_5 = 21.12 kWh
U = C × DoD
16.90 kWh usable
DoD = 80%. Stacks: any number of LV_32, plus at most one LV_16 and one LV_5.
Notes: Without a battery, solar beyond the daytime load is lost, so solar only is sized to D. With a battery, extra solar charges it for the night (U = usable battery energy).
Battery combinations by required kWh: up to 5.12 = LV_5; up to 16 = LV_16; up to 21.12 = LV_16 + LV_5; up to 32 = LV_32; up to 37.12 = LV_32 + LV_5; up to 48 = LV_32 + LV_16; up to 53.12 = LV_32 + LV_16 + LV_5; up to 64 = 2 x LV_32. Ties go to fewer units.
'Full day' mode sizes the battery on E instead of N (the original Home Storage deck's method).

## Slide 4
STEP 4 · NEW BILL
Grid import after solar (kWh per day)
Equation | Solar only | Solar + battery
Generation G = P × Y | 14.40 | 31.20
Direct use = min(G, D) | 12.77 | 12.77
Surplus = G − direct | 1.63 (lost) | 18.43
From battery = min(surplus × η, U, N) | 0 | 15.60
Import / day = E − direct − battery | 15.60 | 0
Import / month = × 30 | 468 kWh | 0 kWh
New bill = Bill(import) | 717 EGP · Tier 5 | 0 EGP
Exported surplus earns nothing: savings count only solar energy the home uses itself.
Notes: Import can never exceed the home's consumption, so the bill with solar is never higher than grid only.

## Slide 5
STEP 5 · ECONOMICS
Price, savings, payback and backup
Equation | Solar only | Solar + battery
Inverter = standard size ≥ max(3, P) | 3 kW | 8 kW
Price = (P × 8,000 + Inverter × 6,000) × 1.10 + C × 13,640 | 46,200 | 398,077
Monthly saving = Bill(M) − Bill(import) | 1,283 | 2,000
Annual saving = monthly × 12 | 15,397 | 24,001
Payback = Price ÷ annual saving | 3.0 years | 16.6 years
Backup hours = U ÷ (E ÷ 24) | none | ≈ 14.3 h
Recommend solar + battery when its payback ≤ 1.15 × solar-only payback
The 10% for installation & BOS applies to PV and inverter only, not to the battery. Backup hours use the average load; air conditioning peaks shorten them.
Notes: Price examples: solar only (3 kWp x 8,000 + 3 kW x 6,000) x 1.10 = 46,200 EGP. Solar + battery (6.5 x 8,000 + 8 x 6,000) x 1.10 + 21.12 x 13,640 = 110,000 + 288,077 = 398,077 EGP.
Standard inverter sizes: 3, 5, 6, 8, 10, 12, 15, 20 kW and up.

## Slide 6
TIER CLIFF
The kWh just above 650 or 1000 are the most valuable to cut
Value per kWh cut = (Bill(M) − Bill(T)) ÷ (M − T), with T = 650 or 1000
4.41
EGP saved per kWh: (2,000 − 1,113.5) ÷ (851 − 650)
2.35
EGP average price today
Notes: Solar sized just to bring consumption under a threshold earns the highest return per kWh.

## Slide 7
REFERENCE
Default assumptions and their sources
Assumption | Default | Source
Night share | 55% | Estimate; needs measured load profiles
PV yield | 4.8 kWh/kWp/day | Cairo ≈ 1,750 kWh/kWp per year
Depth of discharge | 80% | AVESTA LV datasheet: 6,000 cycles at 80%
Round-trip efficiency | 95% | Home Storage deck
Battery price | 13,640 EGP/kWh | Deck: €220 × 62 EGP
PV price | 8,000 EGP/kWp | Deck
Inverter price | 6,000 EGP/kW | Estimate
Installation & BOS | 10% of PV + inverter | Deck: 10–15%
Days per month | 30 | Fixed
All defaults except days per month are editable under “Assumptions & prices” in the tool.